## Slide 1
SDN Evolution and ONF
Platform
Development
2007 – Ethane
2008 – OpenFlow
2009 – FlowVisor, Mininet, NOX
2010 – Beacon
2009 – Stanford
2010 – GENI started and grew to 20 universities
2013 – 20 more campuses to be added
Deployments
Demonstrations
2008-2011 – SIGCOMM
2011 – Open Networking Summit, Interop
2012 –Define SDN research agenda for the coming years
And Beyond
Invention
2007 – Creation of SDN Concept
2017 – ON.Lab and ONF merger
Non-profit, carrier and vendor neutral
Provide technical shepherding, core team
Build community
Many organizations supports

## Slide 2
Northbound
(policy enforcement, conflict resolution)
OpenFlow
NetConf
. . .
Applications
Distributed Core
(scalability, availability, performance, persistence)
Southbound
(discover, observe, program, configure)
Provider
Provider
. . .
Contains user applications
E.g., reactive forwarding, ProxyARP, segment routing, SDN-IP, etc.
Transfer network info to app layer
Provide management interface for controlling lower layer component
Contains many core features
Provide distributed clustering func. for supporting HA and scalability
Provide an abstracted interface for controlling the network infrastructure
Network protocol implementation for managing network elements
E.g., OpenFlow, NetConf
ONOS Architecture (1/2)

## Slide 3
NB Core API
Distributed Core
(state management, notifications, high-availability & scale-out)
SB Core API
Protocols
Providers
Protocols
Providers
Protocols
Providers
Protocols
Providers
Apps
Applications
ONOS Architecture (2/2)

## Slide 4
Device
Link
Host
Topology
Flow Rule
Path
Packet
Statistics
Intent
Application
Leadership
Messaging
Storage
Region
Mastership
Driver
Group
Security
Flow Objective
Event
OpenFlow
NetConf
OVSDB
Core
Cluster
. . .
Proxy ARP
SONA
L2 Forwarding
REST API
GUI
CLI
Network Cfg.
SDN IP / BGP
DHCP
Tunnel
. . .
OSGi / Apache Karaf
Network Virt.
Device Cfg.
Config
UI Extension
Off-platform Apps
Graph
Discovery
Tenant
. . .
OSGi Framework
Non-networking core subsystem
South Bound Interface module
Networking core subsystem
On-platform Applications
On-platform Application Interfaces
Off-platform Applications
ONOS Subsystems (Services)

## Slide 5
ONOS Project at ONF
Mobile
ROADM (Core)
PON OLTs
PON OLTs
Residential
Enterprise
Shared Cloud Infrastructure
VOLTHA
ODTN
Stratum
Trellis
XOS
ONOS
Residential Services
Mobile Services
Enterprise Services

## Slide 6
ONOS Community
Partners
Collaborators

## Slide 7
Q4/14 Avocet
Base Architecture
Q1/15 Blackbird
Performance
Q2/15 Cardinal
ONS Use Cases
SDN-IP
Packet Optical
R-CORD
Q3/15 Drake
ONF ATRIUM
Secure Mode ONOS
VxLAN
Device Configuration
Q4/15 Emu
OPNFV
SONA
AARNET
KREONET-S
Q1/16 Falcon
ONS Use Cases
{A, E, M} CORD
Disaggregated ROADM
Global R&E Deployment
Q2/16 Goldeneye
CPMan Apps
Intents using Flow Objectives
P4 DEMO support
YANG tool chain
Q3/16 Hummingbird
RabbitMQ, Kafka Message
YANG NBI, SBI CODECs
ACTN Traffic Engineering
Q4/16 Ibis
BUCK Build Tool
Trellis Fabric enhancement
LISP SBI support, REST Client, FatTree simulator
Q1/17 Junco
TL1 SBI support
Virtualization support
Regionalization support
Dynamic conf. enhancement
Q2/17 Kingfisher
YANG Tools 2.0
OpenFlow 1.4 support
Intent F/W improment
vRouter, OpenROADM support
Q3/17 Loon
OpenFlow 1.5 SBI
gRPC NBI support
P4 runtime initial support
Q4/17 Magpie
Topo2 initial support
More switch driver support
Q1/18 Nightingale
ISSU initial support
Trellis enhancement (T3)
P4 support enhancment
ONOS Release History
Q2/18 Owl
Coming soon…

## Slide 8
SONA Fabric (Leaf-Spine Fabric)
SONA Fabric Manager
Spine
Spine
Leaf
Leaf
Leaf
Configuration Automation
Traffic Engineering
Fast Failure Detection
Failure Discovery
REST
/ OF

## Slide 9
SONA Fabric - BGP

## Slide 10: SONA Fabric - OF
Pure OpenFlow based Leaf-Spine Fabric Solution
Supports ECMP, Failure detection & auto recovery
Physical + Virtual Network Integration

## Slide 11
SONA Fabric - Deployment
AI Cloud Test-bed : Two Racks with 20+ servers (10G) and 4 Storages (40G)

## Slide 12
vFlow Statistics
  Collect VM to VM real-time flow statistic
  Stats collection is realized using OpenFlow standards protocol (no extra overhead!)
  Seamless integration with monitoring systems through various NBIs
    REST, Kafka, gRPC, influxDB, etc.
  Realized through Telemetry app
  No additional software installations are required at OpenStack side
  No additional hardware installations are required at compute/control node
  Open source!
SDN Controller
Telemetry
…
REST
Kafka
gRPC
influxDB
…
Host
Host
OpenFlow
SONA Fabric - Monitoring

## Slide 13
SONA Fabric - Monitoring
Traffic Monitoring with TINA

## Slide 14
Grafana UI
SONA Fabric - Monitoring

## Slide 15
SONA Fabric – Open Source
All codes are 100% open
https://github.com/opennetworkinglab/onos
https://wiki.onosproject.org/display/ONOS/SimpleFabric+Application

## Slide 16: Thank you